## Slide 1: LASER BLOOD FLOW MEASURENT & PORT WINE STAIN
Department of Medical Instrumentation Engineering Techniques, Electrical Engineering Technical College, Middle Technical University(MTU),Baghdad-Iraq
Postgraduate(M.Sc. Tech.)
Second Semester(2018-2019)
Dr. Jannan Fadel

## Slide 2: Outline
Why using laser blood flow measurement .
What volume of tissue does the LDF measure?
How does LDF work ?
What are the advantages of LDF?
Probes and Applications.
The Backscatter Signal.
What is a Port Wine Stain.
What Causes a Port Wine Stain?
Port Wine Stain removal.
The Difference Between Flat and Thick Vascular lesions.

## Slide 3: Why using laser blood flow measurement
A Laser Doppler Flowmeter (LDF) works by reading the frequency of the oscillation produced by the Doppler frequency shift of the red blood cells in a peripheral tissue and translates the frequency to an intensity oscillation.
Laser Doppler Flowmetry is an inexpensive, noninvasive
method of measuring the continuous circulation of
blood flow on a microscopic level.

## Slide 4: What volume of tissue does the LDF measure?
The actual measurement sampling volume or depth can only be determined by identifying precisely which blood vessels and erythrocytes have interacted with the remitted light , is principally dependent on two parameters; namely the optical scattering and optical absorption coefficients of the tissue under observation , the mean sampling depth is in the region 0.5-1.0 mm with a concomitant sampling volume in the region 0.3-0.5 mm3.

## Slide 5: How does LDF work ?
Tissue is illuminated by low power laser light; the light is scattered by the static tissue structures and moving blood cells
Portion of the light is Doppler shifted
Adjacent fiber optic detects un-shifted and
Doppler-shifted light
Signal is processed to give a parameter related to tissue blood perfusion

## Slide 6: What are the advantages of LDF?
The LDF technique offers substantial advantages over other methods in allowing the continuous measurement of microvascular blood perfusion.
The LDF may be used non-invasively (since the probe is not actually required to touch the surface of the tissue) and in no way harms or disturbs the normal physiological state of the microcirculation
LDF is both highly sensitive and responsive to local blood perfusion and is also versatile and easy to use for continuous monitoring.
Continuous/real-time – response time 0.15s
Sensitive to small changes
May be used non-invasively , On skin or organ surface where exposed
Small probe dimensions Minimal trauma where used invasively

## Slide 7: Probes and Applications
Surface and Digit Probes
Suturable and Miniature Surface Probes
Needle and Pencil Probes
Single Fiber Probes

## Slide 8: Surface and Digit Probes
Applications:
Skin, large organ,
Noninvasive, Adhesive ring

## Slide 9: Suture & Miniature Surface Probes
Applications:
Small organ, non invasive

## Slide 10: Needle Probes
Applications:
Invasive tissue measurement;
e.g. Cerebral monitoring

## Slide 11: Single Fiber Probes
Applications:
Chronic Implantation

## Slide 12: The Backscatter Signal
Diagnostic Signal
Suggests probe location changed
Low back scatter Flow signal is cut out
Probe has become detached
Faulty probe
High back scatter
Probe detached, facing a reflective surface (e.g. bone)

## Slide 13: What is a Port Wine Stain
Port wine stains, also known as nevus flammeus , are a unique type of birthmark that appears as a red or pink mark on the skin. These birthmarks are most commonly found on the face, head, arms or legs. they can affect a person’s self-confidence

## Slide 15: What Causes a Port Wine Stain?
Port wine stains are caused by overactive blood flow through the tiny vessels in the body. This excessive blood flow causes the vessels to enlarge, and the excess blood is what creates the actual mark on the skin. Certain genetic factors seem to influence a person’s risk for having a port wine stain.

## Slide 16: Port Wine Stain removal
Port Wine Stains are usually treated with a pulsed dye laser , a laser machine that is able to produce Incredibly short , very intense bursts of laser energy . Because of the intensity of Port Wine Stains an Laser Treatment , there is a much longer recovery period associated With treating Wine Stains than with other types of laser machine procedures , especially when a pulsed dye laser is used.
Ordinary treatment of Port Wine Stain can have some side effects . If any normal skin is affected by the laser , blisters develop - this means that Port Wine Stain Removal with a pulsed dye laser is not suitable for beginning clinicians . and has a sunburn feeling for some days.

## Slide 17: The Difference Between Flat and Thick Vascular lesions
Flat lesions are much easier to treat with a laser, as it is mostly a color improvement that needs to occur. Port Wine Stains usually start out flat and pinkish, and gradually thicken and can become no dulated in adulthood.
If they are left untreated, they can start bleeding, or cause loss of function when they are located near a patients eye, nose or ear.